DATA FORMAT                                    
                                                                                
                                                                                
                Format for the ASCII version of Helios A & B                    
                                                                                
                8 Second Averaged Magnetic Field Vector Data                    
                                                                                
                     NSSDC ID: 74-097A-01E & 76-003A-01E
                                                                                
                                                                                
     BYTES                  DESCRIPTION OF SCIENCE RECORD                       
    -------    -----------------------------------------------------            
     1 - 3     Type of  record                                                  
                        100   - tape header record                              
                          9   - science record (average tapes)                  
                        999   - tape trailer record                             
     4 - 7      # of days since launch year                                     
                  (1 = 1st Jan 1974 for HE-A / 1st Jan 1976 for HE-B)           
     8 - 22     Fraction of day (decimal)                                       
    23 - 25     # of vectors in record                                          
    26 - 28     Vector rate ( 8/sampling rate )                                 
    29 - 31     Format #                                                        
    32 - 37     Bit rate                                                        
    38 - 43     Distribution mode                                               
    44 - 58     Vector step time in fraction of day                             
    59 - 61     Mission (Helios A = 90, Helios B = 91)                          
    62 - 74     Ecliptical latitude of s/c spin axis in radians                 
    75 - 87     Ecliptical longitude of s/c spin axis in radians                
    88 - 100    Ecliptical longitude, counted from mean equinox,                
                 of Helios in radians                                           
   101 - 113    Distance from sun in A.U.                                       
   114 - 126    Heliographic latitude of Helios in radians                      
   127 - 139    Helios - Sun - Earth angle                                      
   140 - 152    Offset in  X in gamma                                           
   153 - 165    Offset in  Y in gamma                                           
   166 - 178    Offset in  Z in gamma                                           
   179 - 184    Misalignment angle lambda in 1/10 degrees                       
   185 - 190                       alpha  in 1/10 degrees                       
   191 - 196                       gamma  in 1/10 degrees                       
   197 - 202                       beta   in 1/10 degrees                       
   203 - 208                       epsilon in 1/10 degrees                      
   209 - 214    Mean deviation * sqrt(3) of last misalignment                   
                  calculation in 1/100 degrees                                  
   215 - 229    Trip light time in fraction of day                              
   230 - 244    Spin period in fraction of day                                  
                                                                                
   245 - 249    Field component XSE in 1/100 gamma                              
   250 - 254    Field component YSE in 1/100 gamma                              
   255 - 259    Field component ZSE in 1/100 gamma                              
   260 - 264    Sigma X             (    "  "     )                             
   265 - 269    Sigma Y             (    "  "     )                             
   270 - 274    Sigma Z             (    "  "     )                             
   275 - 279    Sigma F             (    "  "     )                             
   280 - 284    F (computed from XSE, YSE, ZSE above) in 1/10 gamma             
   285 - 292    Status indicators   (see General Remarks)                       
   N repetitions of bytes 245-292, N as specified in bytes 23-25.               
                                                                                
                                                                                
     BYTES          DESCRIPTION OF HEADER RECORD                                
    -------    -----------------------------------------------------            
     1 - 3     Type of  record                                                  
                        100   - tape header record                              
                          9   - science record (average tapes)                  
                        999   - tape trailer record                             
     4 - 6     Field always equals 20                                           
     7 - 42    Header specifying spacecraft.                                    
               **** E2ADR TAPE HEADER/HELIOS A ****                             
               **** E2ADR TAPE HEADER/HELIOS B ****                             
                                                                                
                                                                                
                                                                                
  GENERAL REMARKS:                                                              
                                                                                
   The tapes are 9 track, 6250 BPI, written in ASCII.                           
                                                                                
   This ASCII version was created in March 1996 by NSSDC from the original      
   binary data.  We have retained the original file structure of the data;      
   there is a tape header record, followed by data records, perhaps followed    
   by a tape trailer record.  In the data records, an End-Of-File is written    
   after every full hour if there are at least 10 records in the file.          
                                                                                
   Maximum record length is 3364 bytes.                                         
                                                                                
   For type 9 records times refer to the middle of the first                    
   average interval.                                                            
                                                                                
                                                                                
   Status Indicators:                                                           
                                                                                
           Byte 1    Byte 2   Byte 3       Byte 4                               
                                                                                
           quality   quality  indication   flip status                          
           (best)    (worst)   for # of                                         
          (ave.tape)          vectors used                                      
                              for average                                       
                                                                                
       Quality values range from 0 to 7.  0 corresponds to fine and 6 to        
       poor quality while 7 flags missing data.  Vectors with qualities         
       up to 3 can be treated as good.                                          
                                                                                
       Indication for # of vectors used for average :                           
             0 : : = 0                 4 : : < 50                               
             1 : : < 5                 5 : : < 100                              
             2 : : < 10                6 : : < 500                              
             3 : : < 25                7 : : < 500                              
                                                                                
       Flip Status 0 means unflipped status (u parallel spin axis),             
       while value of 1 means flipped.                                          
                                                                                
       There was one instance where the original binary status word bits        
       were equal to hex 'FFFF', which results as an '*' in this field          
       during the conversion routine. The asterisk remains on the tape          
       containing day 760, and is located in file 777, record 1 as a            
       signal to the user.